OPTIONS:

SPECS FOR 1800 EFQ EXTENSION

LENGTH:	48"

WIDTH:	26"

Equipped with:	3	Idler Rollers

1	18" Hot Asphalt Belt

To be spliced into conveyor belt.

Attaches to the right side of the conveyor. (passenger side)

Removable hopper sides.

Folds up for transporting.

1/4" Formed Channels

11 ga Formed Hopper with 7 ga Gussets

SPECS FOR MODEL 1218 P POWER UNIT

PUMP: Direct engine driven pump, rated at 10 GPM @ 3600 RPM, 2000 PSI.

ENGINE: 16 HP Briggs. Electric start with recoil backup. Battery not included.

VALVE: Manually adjusted flow control. Optional electric valve is required to have cab control of belt on-off.

HYDRAULICS: 10 gallon reservoir with filter and suction strainer.

SPECS FOR MODEL 1800SL SANDER

SPINNER: 18” diameter with 6 flights, welded steel.

SPREAD CONTROL: 1 removable baffle for control of coverage. Detachable door allows you to sand 1 or 2 lanes of highway.

DRIVE: Motor coupled directly to spinner.

REAR REVERSING VALVE

A valve capable of reversing the conveyor, with speed control in either direction. The valve mounts on the rear of the conveyor for easy access by the operator. Hoses to the valve are proected by a hose tube fastened under the conveyor. The valve has an inlet relief set at 2000 PSI.

MODEL 1218 SANDBAG ATTACHMENT

With the Sandbag Attachment installed, a standard sandbag can be filled in 2 seconds.

MODEL 1218LA LEVELING ASSEMBLY

The 2’ wide leveling assembly allows you to apply and level the material in one easy step to put the finishing touch on your road shouldering operation. This assembly comes in either manual or hydraulic manifold.

DEFLECTOR PLATE

The quick attaching Deflector Plate can be mounted on either side of the conveyor. It spreads the material as it is conveyed for a finished look.

GATE OPENER

Fast opening gate for right or left hand discharge. Both gates adjust in 1” increments or can be equipped with optional hydraulic motors.